## Slide 1: 18-799: Applied Computer Vision Spring 2026
Image Formation

## Slide 2: Objectives
In today’s class we will learn
  Homogeneous Coordinates and transformation
  Geometric primitive
  Geometric Image formation
  Photometric image formation

## Slide 3: Homogeneous Coordinates
In computer vision, image formation is a chain of transformations:
If each step is linear:
  then the whole pipeline collapses into:

## Slide 4: Homogeneous Coordinates
Let’s consider the function , where:
Can we represent with a matrix?
  That’s, is there a matrix A such that:

## Slide 5: Homogeneous Coordinates
Points in Euclidean Coordinates
  In standard 2D space, a point is represented as a vector
Points in Homogeneous Coordinates
  The same point is represented by the augmented vector
More generally, the Euclidean point corresponds to the entire equivalence class
All such homogeneous vectors represent the same geometric point after normalization.

## Slide 6: Homogeneous Coordinates
Euclidean point corresponds to the entire equivalence class in homogeneous coordinates:
  Since can be anything (then could be re-written
To convert a homogeneous vector back to inhomogeneous form, we divide by the last coordinate
The corresponding inhomogeneous point is obtained by dropping the last coordinate:

## Slide 7: Homogeneous Coordinates
Let’s re-consider the function , where:
Can we represent with a matrix?
  That’s, is there a matrix A such that:

## Slide 8: Geometric primitive
Geometric primitives are the basic building blocks used to describe 3D shapes
Examples: Points, lines, planes

## Slide 9: 2D Points
2D points can be written in inhomogeneous coordinates as
or in homogeneous coordinates as where is called projective space.
Homogeneous vectors that differ only by scale are considered equivalent and define an equivalence class.

## Slide 10: 2D Points
  An inhomogeneous vector is converted to a homogeneous vector as follows
with augmented vector .
  To convert in the opposite direction we divide by :
  Homogeneous points whose last element isare called ideal points or points at infinity. These points can't be represented with inhomogeneous coordinates

## Slide 11: 2D Lines
2D lines can also be expressed using homogeneous coordinates
:
An exception is the line at infinity which passes through all ideal points.

## Slide 12: Cross Product
Cross product of two vector:
Cross product expressed as the product of a skew-symmetric matrix and a vector
See Levi-Civita symbol for more info.

## Slide 13: Cross Product
In homogeneous coordinates, the intersection of two lines is given by:
Similarly, the line joining two points can be compactly written as:

## Slide 14: 2D Line: Example

## Slide 15: 2D Line: Example

## Slide 16: 2D Conics
More complex algebraic objects can be represented using polynomial homogeneous equations.
For example, conic sections (arising as the intersection of a plane and a 3D cone) can be written using quadric equations:

## Slide 17: 3D Quadrics
Paschalidou, Ulusoy and Geiger: Superquadrics Revisited: Learning 3D Shape Parsing beyond Cuboids. CVPR, 2019
The 3D analog of 2D conics is a quadric surface:

## Slide 18: Translation
(2D Translation of the Input, 2 DoF)
Using homogeneous representations allows to chain/invert transformations
Augmented vectors can always be replaced by general homogeneous ones

## Slide 19: Affine
Equivalent to 2D Linear Transformation, 6 DoF
is an arbitrary matrix
Parallel lines remain parallel under affine transformations

## Slide 20: Projective
Homography, 8 DoF
is an arbitrary homogeneous matrix (specified up to scale)
Projective transformations preserve straight lines
Notes: Sia

## Slide 21: Projective
©commons.wikimedia.org
Notes: Sia

## Slide 22: Projective
A homography is defined in homogeneous coordinates as
Write the point in homogeneous form:
Let
We now have:
Notes: Sia

## Slide 23: Projective
Homogeneous coordinates represent points up to scale. To recover Euclidean coordinates, we divide by the last component:
Substituting gives exactly:
Notes: Sia

## Slide 24: 2D Transformation

## Slide 25: 3D Transformation

## Slide 26: Geometric Image Formation

## Slide 27
Homogeneous Coordinates
Inhomogeneous Coordinates
Augmented Vector
Homogeneous Vector
2D Points

## Slide 28: Perspective Projection
In perspective projection, we have:
, where
Note that this projection is linear when using homogeneous coordinates.
After the projection it is not possible to recover the distance of the 3D point from the image.
Calibration matrix

## Slide 29: Perspective Projection

## Slide 30: Perspective Projection
The complete perspective projection model is given by:
The left submatrix of the projection matrix is called calibration matrix
The parameters of are called camera intrinsics (as opposed to extrinsic pose)
Here, and are independent, allowing for different pixel aspect ratios
The skew arises due to the sensor not mounted perpendicular to the optical axis
In practice, we often set and , but model

## Slide 31: Chaining Transformation
Let be the calibration matrix (intrinsics) and the camera pose (extrinsics).
We chain both transformations to project a point in world coordinates to the image:

## Slide 32: Perspective Projection
Image Magnification:
Image size inversely proportional to depth
f: Effective focal length
z

## Slide 33: Perspective Projection
Vanishing point

## Slide 34: Perspective Projection
Vanishing point:
https://commons.wikimedia.org/wiki/File:1_point_perspective.svg

## Slide 35: Lens
f
Focal length (f): It determines the lens’ bending power
This Lens’ law:
Magnifiction (m):
https://en.wikipedia.org/wiki/Focal_length

## Slide 36: Lens
Aperture: Area of the lens receiving light

## Slide 37: Lens
Aperture: Area of the lens receiving light
f-number: a measure of the light-gathering ability of a camera lens
it equals focal length divided by the aperture.
Aperture:
where is called the -Number of lens.

## Slide 38: Lens Defocus
Image Plane
Aperture
How to find the blur circle

## Slide 39: Lens Distortion
Chromatic Aberration
Refractive index (and hence focal length) of lens is different for different wavelengths.

## Slide 40: Lens Distortion
Vignetting

## Slide 41: Photometric Image Formation
How an image is formed in terms of pixel intensities and colors.
Light is emitted by one or more light sources and reflected or refracted (once or multiple times) at surfaces of objects (or media) in the scene

## Slide 42: Rendering Equation
Let denote a 3D surface point, the viewing direction and the incoming light direction.
The rendering equation describes how much of the light with wavelength arriving at is reflected into the viewing direction :
  is the unit hemisphere at normal
  The bidirectional reflectance distribution function defines how light is reflected at an opaque surface.
  only for light emitting surfaces

## Slide 43: Global Illumination
Modeling one light bounce is insufficient for rendering complex scenes
I Light sources can be shadowed by occluders and rays can bounce multiple times
I Global illumination techniques also take indirect illumination into account

## Slide 44: Diffuse and Specular Reflection

## Slide 45: Image Sensor
Physical light transport in the camera lens/body
Photon measurement and conversion on the sensor chip
Image signal processing (ISP) and image compression

## Slide 46: Image Sensor
I CCDs move charge from pixel to pixel and convert it to voltage at the output node
I CMOS images convert charge to voltage inside each pixel and are standard
https://meroli.web.cern.ch/lecture_cmos_vs_ccd_pixel_sensor.html

## Slide 47: Image Sensor
Color Filter:
To measure color, pixels are arranged in a color array, e.g.: Bayer RGB pattern
I Missing colors at each pixel are interpolated from the neighbors (demosaicing)

## Slide 48: Image Sensor
Color Filter:
To measure color, pixels are arranged in a color array, e.g.: Bayer RGB pattern
I Missing colors at each pixel are interpolated from the neighbors (demosaicing)

## Slide 49: Reference
https://uni-tuebingen.de/fakultaeten/mathematisch-naturwissenschaftliche-fakultaet/fachbereiche/informatik/lehrstuehle/autonomous-vision/lectures/computer-vision/